Left and right line spools, rotating individually around a shared, fixed an axle. One coupled to the outer-ring of a planetary gear, the other coupled to the planet-ring, with a relative gear ratio such that when the sun gear is fixed, this coupling requires the left and right spools to rotate at the same rate. In the exhibit embodiment, this coupling is via chain-wheels and chains. Rotation of the sun gear affects an adjustment of the relative angular position of the left and right kite line spools.
One or both of these spools is coupled to a third spool. This coupling is either fixed, or via a free-wheel mechanism such that the third spool can not effect a positive torque on the kite spools (in other words, push the kite line out). If both kite line spools are connected to the third spool, the couplings need to be via free-wheel in order to allow adjustment of the relative angular position of the left and right spools.
The entire steering subsection is anchored into the ground in such a way that it is free to pivot about an axis perpendicular to the ground, changing angle A as pictured in diagram 1.
A transmission line runs from the center spool in the steering subsystem, along the axis of the steering subsystem's rotation, to a spool in the Drive/Recoil subsystem (D/R) . The force interaction between the D/R and the kite lines is tensile along this transmission line.

The transmission line spool in the D/R subsystem is coupled to the D/R sun gear in the planetary gear in the D/R subsystem. As in the exhibit embodiment, this may be via a chain-wheel cog hub, or another mechanism that allows changing the gear ratio of this coupling.

The outer ring of the D/R planetary gear is coupled to a flywheel. In the exhibit embodiment, this is via chain and chain-wheel.

The planet ring of the D/R planetary gear is coupled to a component that produces a drag, for example a generator. Both of these are also coupled to the sun gear/chain-wheel cog hub. This coupling is via freewheel, so that it can rotate clockwise (as pictured) at a rate greater than the cog hub.

The ratio of the coupling between the sun gear and the planet ring effected when the freewheel is engaged can be 1 to 1, or N to 1 where N is any number between 1/10 and 10.